## Slide 1
DATA ANALYST CAPSTONE PROJECT
Solar Production Forecasting
with Machine Learning
From weather signal to next-day forecast: modeling, temporal validation, and deployment on a Streamlit dashboard.
26,676
daily observations, 2020 to 2026
12
French regions covered
36
Input features
Solar Production Forecasting · Machine Learning · Streamlit Dashboard
01

## Slide 2
01 · CONTEXT
Why forecast solar production?
Solar output is entirely weather dependent: without a forecast, every gap between expected and actual production has a direct cost.
!
Total intermittency
Unlike nuclear or gas, solar production cannot be dispatched on demand: it depends entirely on tomorrow's radiation.
A reliable next-day forecast means anticipating production before it happens, instead of just reacting to it.
Selling electricity
Avoid unfavorable buybacks or underpriced sales on wholesale markets.
Battery management
Optimize charge/discharge cycles and extend storage system lifespan.
Preventive maintenance
Detect yield anomalies (dirty or faulty panels) and plan interventions.
Grid management
Anticipate high production days to reduce reliance on gas.
Solar Production Forecasting · Machine Learning · Streamlit Dashboard
02

## Slide 3
02 · DATA & METHOD
Data & Method
Three data sources joined by region and day, a 5-step pipeline, with time-respecting validation (no shuffling).
26,676 rows
Meteo-France
Radiation, temperature, humidity, wind... by region and day, 2020 to 2026.
12 regions
RTE, solar production
Half-hourly production aggregated into daily TWh by region.
SDES
Installed capacity (MW)
Installed photovoltaic capacity by region, used to normalize production.
METHODOLOGY
1
Feature
engineering
Lags J-1/J-2/J-3, 7 day rolling means, seasonality (sin/cos).
2
Baseline &
raw regression
Naive persistence vs. regression without feature engineering.
3
Temporal
validation
TimeSeriesSplit (5 folds), pipeline refit on every fold.
4
GridSearchCV
Hyperparameter search (RMSE) across all models.
5
Final model
selection
R2/MAE/RMSE train vs test comparison, prioritizing stability.
Solar Production Forecasting · Machine Learning · Streamlit Dashboard
03

## Slide 4
02 · DATA & METHOD
The full pipeline, end to end
1 · DATA COLLECTION
2 · PREPARATION & ANALYSIS
3 · MODELING & COMPUTATION
Meteo-France
Weather data, 2020 to 2026.
RTE France
Solar production, 2020 to 2026.
Installed PV capacity
Capacity by region (SDES).
GeoJSON
12 French regions.
Regional mapping
Grid points mapped to regions.
Data harmonization
Common period: 2020 to 2026.
Data integration
Weather + production + capacity.
Consolidated dataset
Region x day, 2020 to 2026.
Exploratory analysis
Correlations, trends, seasonality.
Machine Learning
Regression modeling.
Radiation forecast
Predicts next-day visible radiation.
Production estimate
Radiation → kWh/m² at 20% efficiency.
Solar Production Forecasting · Machine Learning · Streamlit Dashboard
04

## Slide 5
03 · EXPLORATORY ANALYSIS
What explains solar production
Correlations between weather variables and production per capacity, across 26,676 observations.
0.93
Visible radiation
Strongest correlation with production.
-0.75
Relative humidity
Negative correlation (cloudier sky).
0.87
Potential evapotranspiration
Strong positive correlation, tied to sunshine.
Solar Production Forecasting · Machine Learning · Streamlit Dashboard
05
Correlation Matrix | Meteorological Variables vs Solar Production
Snowfall
Rainfall
Avg Temp
Wind Speed
Spec. Humidity
Atm. Radiation
Visible Rad.
Rel. Humidity
Total ET
Potential ET
Prod / Capacity
1.00
0.27
-0.23
0.07
-0.18
-0.11
-0.18
0.13
-0.14
-0.17
-0.21
0.27
1.00
0.01
0.27
0.15
0.27
-0.30
0.35
-0.07
-0.20
-0.33
-0.23
0.01
1.00
-0.14
0.92
0.77
0.65
-0.42
0.60
0.80
0.62
0.07
0.27
-0.14
1.00
-0.14
-0.07
-0.30
0.17
-0.12
-0.18
-0.31
-0.18
0.15
0.92
-0.14
1.00
0.90
0.42
-0.11
0.48
0.59
0.41
-0.11
0.27
0.77
-0.07
0.90
1.00
0.16
0.19
0.28
0.35
0.14
-0.18
-0.30
0.65
-0.30
0.42
0.16
1.00
-0.79
0.80
0.94
0.93
0.13
0.35
-0.42
0.17
-0.11
0.19
-0.79
1.00
-0.47
-0.76
-0.75
-0.14
-0.07
0.60
-0.12
0.48
0.28
0.80
-0.47
1.00
0.75
0.76
-0.17
-0.20
0.80
-0.18
0.59
0.35
0.94
-0.76
0.75
1.00
0.87
-0.21
-0.33
0.62
-0.31
0.41
0.14
0.93
-0.75
0.76
0.87
1.00
Snowfall
Rainfall
Avg Temp
Wind Speed
Spec. Humidity
Atm. Radiation
Visible Rad.
Rel. Humidity
Total ET
Potential ET
Prod / Capacity

## Slide 6
04 · MODELING
Why lags matter: ACF & PACF
Today's radiation strongly explains tomorrow's, but most of the signal is already captured by J-1.
Solar Production Forecasting · Machine Learning · Streamlit Dashboard
06

## Slide 7
05 · MODEL CHOICE
From baseline to final model
8 models evaluated, from the naive baseline to XGBoost. Ridge chosen as final model.
1
Linear regression
Baseline run, no feature engineering. R2 = 0.761
2
Add lags & rolling means
J-1, J-2, J-3 plus rolling means. R2 = 0.778
3
Add seasonality
Calendar encodings (sin/cos of day of year). R² = 0.792
4
GridSearchCV x TimeSeriesSplit
Lasso, Ridge, RF, XGBoost tuned on 5 expanding-window folds.
5
Ridge (L2) selected
−15% error vs baseline (RMSE 437 → 371), with a far smaller train-test gap than RF/XGBoost.
Model | R2 | MAE (J/cm²) | RMSE (J/cm²)
Naive baseline (persistence) | 0.708 | 316 | 437
LR, no feature engineering | 0.761 | 301 | 395
LR, with lags (J-1/J-2/J-3) | 0.778 | 288 | 381
LR, lags + seasonality | 0.792 | 279 | 368
Lasso (L1) | 0.788 | 282 | 372
Ridge (L2), FINAL MODEL | 0.789 | 282 | 371
Random Forest | 0.800 | 274 | 362
XGBoost | 0.801 | 272 | 360
Solar Production Forecasting · Machine Learning · Streamlit Dashboard
07

## Slide 8
05 · MODEL CHOICE
Why Ridge, not Random Forest or XGBoost?
RF and XGBoost gain only marginally more test R2, with a much wider train/test gap.
Model | R2 train (CV) | R2 test (CV) | Train-test gap
Ridge, chosen | 0.767 | 0.742 | 0.025
Random Forest | 0.855 | 0.740 | 0.115
XGBoost | 0.818 | 0.748 | 0.069
Ridge stays stable fold to fold (gap of about 0.02). RF and XGBoost barely gain more in test for a 3 to 5x larger gap: we prioritize robustness.
A physical limit, corrected
Ridge, like any linear model, has no awareness that radiation can't be negative: it can predict slightly below 0 on low-radiation winter days. Predictions are therefore clipped to 0 (np.clip) before display and export, a correction that can only reduce error, never increase it.
Solar Production Forecasting · Machine Learning · Streamlit Dashboard
08

## Slide 9
06 · RESULTS
Forecast vs reality: final model (Ridge)
2025 predicted vs. actual radiation, a representative year from the 2021-2026 out-of-fold evaluation (22,150 predictions).
Solar Production Forecasting · Machine Learning · Streamlit Dashboard
09

## Slide 10
06 · RESULTS
Forecast vs reality: residual analysis
Residuals over the full 2021-2026 test period (predicted minus actual, national daily mean): errors stay centered near zero.
Solar Production Forecasting · Machine Learning · Streamlit Dashboard
10

## Slide 11
07 · LIMITATIONS & NEXT STEPS
What's left to improve
The current model's known limitations, and the paths considered to go further.
LIMITATIONS
NEXT STEPS
A single horizon (J+1)
No J+2/J+7 forecast for longer-term planning.
Observed weather, not forecasts
The model uses measured weather for today; a real J+1 forecast would need Météo-France forecast data.
Radiation as a proxy
Production is a theoretical 20% conversion per m², not RTE's actual output.
Extended forecasts, J+2/J+3/J+7
For longer-term energy planning.
Use weather forecasts as inputs
Move from a retrospective model to an operational forecast.
Predict actual production
Target RTE output (TWh or capacity factor) directly. This also enables anomaly detection.
Solar Production Forecasting · Machine Learning · Streamlit Dashboard
11

## Slide 12
SUMMARY
From raw data to a production forecasting dashboard
26,676 observations, 12 regions, 6 years of Meteo-France x RTE x SDES data
Time-respecting validation (TimeSeriesSplit + GridSearchCV). Ridge chosen for its stability: −15% error vs "tomorrow = today" (R² ≈ 0.79)
Streamlit dashboard in production: interactive EDA and next-day forecasts
Thank you for your attention.
Now, a walkthrough of the Streamlit dashboard, followed by questions.
Solar Production Forecasting · Machine Learning · Streamlit Dashboard
12