## Slide 1
DATA ANALYST CAPSTONE PROJECT
Next-Day Solar Radiation Forecasting as a Proxy for Solar Production
From weather signal to next-day forecast: modeling, temporal validation, and deployment on a Streamlit dashboard.
26,676
daily observations, 2020 to 2026
12
French regions covered
36
Input features
Solar Production Forecasting · Machine Learning · Streamlit Dashboard
01

## Slide 2
01 · CONTEXT
Why forecast solar production?
Solar output is entirely weather dependent: without a forecast, every gap between expected and actual production has a direct cost.
!
A fast-growing, intermittent source
Unlike nuclear or gas, solar can't be dispatched on demand: it depends on tomorrow's radiation. The more the fleet grows, the more producers and grid operators need a reliable next-day forecast.
Selling electricity
Avoid unfavorable buybacks or underpriced sales on wholesale markets.
Battery management
Optimize charge/discharge cycles and extend storage system lifespan.
Preventive maintenance
Detect yield anomalies (dirty or faulty panels) and plan interventions.
Grid management
Anticipate high production days to reduce reliance on gas.
32.6 TWh
produced in 2025,
×2.6 since 2020
30.4 GW
installed end of 2025,
+5.9 GW in one year
48 GW
PPE3 target for 2030,
55–80 GW by 2035
Sources: RTE eCO2mix · RTE, Bilan électrique 2025 · PPE3 decree, February 2026
Solar Production Forecasting · Machine Learning · Streamlit Dashboard
02

## Slide 3
01 · PROJECT FRAMING
Specifications, planning & budget
Scoped like a request from a business team: a 4-week project, 3 people part-time, 21 May → 18 June 2026.
Specifications
CLIENT
Solar producer or grid operator
NEED
Anticipate next-day solar production, per region
SCOPE
12 mainland regions · J+1 horizon · daily data 2020-2026
DELIVERABLES
Forecasting model · Streamlit dashboard · documentation
CONSTRAINTS
Public data only · no infrastructure budget
SUCCESS CRITERION
Outperform the naive “tomorrow = today” forecast · result: −15% error
Backward schedule · presentation on 18 June
21 May
28 May
4 Jun
11 Jun
Scoping & data collection
Preparation, spatial join & EDA
Modeling & validation
Dashboard & deployment
Phases overlapped: first models on the raw dataset, then on the full one.
Budget · estimate
30 days
3 people, half-time, 4 weeks
≈ €13.5k
at €450/day (assumption)
€0
infrastructure & data
Production version would add weather forecasts, paid hosting and quarterly maintenance.
Solar Production Forecasting · Machine Learning · Streamlit Dashboard
03

## Slide 4
02 · DATA & METHOD
The full pipeline, end to end
1 · DATA COLLECTION
2 · PREPARATION & ANALYSIS
3 · MODELING & COMPUTATION
Meteo-France
Weather data, 2020 to 2026.
RTE France
Solar production, 2020 to 2026.
Installed PV capacity
Capacity by region (SDES).
GeoJSON
12 French regions.
Regional mapping
Grid points mapped to regions.
Data harmonization
Common period: 2020 to 2026.
Data integration
Weather + production + capacity.
Consolidated dataset
Region x day, 2020 to 2026.
Exploratory analysis
Correlations, trends, seasonality.
Machine Learning
Regression modeling.
Radiation forecast
Predicts next-day visible radiation.
Production estimate
Radiation → kWh/m² at 20% efficiency.
Solar Production Forecasting · Machine Learning · Streamlit Dashboard
04

## Slide 5
03 · EXPLORATORY ANALYSIS
What explains solar production
Correlations between weather variables and production per capacity, across 26,676 observations.
0.93
Visible radiation
Strongest correlation with production.
-0.75
Relative humidity
Negative correlation (cloudier sky).
0.87
Potential evapotranspiration
Strong positive correlation, tied to sunshine.
Solar Production Forecasting · Machine Learning · Streamlit Dashboard
05
Correlation Matrix | Meteorological Variables vs Solar Production
Snowfall
Rainfall
Avg Temp
Wind Speed
Spec. Humidity
Atm. Radiation
Visible Rad.
Rel. Humidity
Total ET
Potential ET
Prod / Capacity
1.00
0.27
-0.23
0.07
-0.18
-0.11
-0.18
0.13
-0.14
-0.17
-0.21
0.27
1.00
0.01
0.27
0.15
0.27
-0.30
0.35
-0.07
-0.20
-0.33
-0.23
0.01
1.00
-0.14
0.92
0.77
0.65
-0.42
0.60
0.80
0.62
0.07
0.27
-0.14
1.00
-0.14
-0.07
-0.30
0.17
-0.12
-0.18
-0.31
-0.18
0.15
0.92
-0.14
1.00
0.90
0.42
-0.11
0.48
0.59
0.41
-0.11
0.27
0.77
-0.07
0.90
1.00
0.16
0.19
0.28
0.35
0.14
-0.18
-0.30
0.65
-0.30
0.42
0.16
1.00
-0.79
0.80
0.94
0.93
0.13
0.35
-0.42
0.17
-0.11
0.19
-0.79
1.00
-0.47
-0.76
-0.75
-0.14
-0.07
0.60
-0.12
0.48
0.28
0.80
-0.47
1.00
0.75
0.76
-0.17
-0.20
0.80
-0.18
0.59
0.35
0.94
-0.76
0.75
1.00
0.87
-0.21
-0.33
0.62
-0.31
0.41
0.14
0.93
-0.75
0.76
0.87
1.00
Snowfall
Rainfall
Avg Temp
Wind Speed
Spec. Humidity
Atm. Radiation
Visible Rad.
Rel. Humidity
Total ET
Potential ET
Prod / Capacity

## Slide 6
04 · MODELING
Past radiation matters: ACF & PACF
Today’s radiation strongly explains tomorrow’s: the signal is concentrated in J‑1, with a last significant value at J‑3.
Solar Production Forecasting · Machine Learning · Streamlit Dashboard
06

## Slide 7
05 · MODEL CHOICE
From baseline to final model
8 models evaluated, from the naive baseline to XGBoost, scored on unseen 2024–2026 data. Ridge chosen as final model.
1
Linear regression
Baseline run, no feature engineering. R² = 0.761
2
Add lags & rolling means
J-1, J-2, J-3 plus rolling means. R² = 0.778
3
Add seasonality
Calendar encodings (sin/cos of day of year). R² = 0.792
4
GridSearchCV x TimeSeriesSplit
Lasso, Ridge, RF, XGBoost tuned on 5 expanding-window folds.
5
Ridge (L2) selected
−15% error vs baseline (RMSE 437 → 371), with a far smaller train-test gap than RF/XGBoost.
Model | R² | MAE (J/cm²) | RMSE (J/cm²)
Naive baseline (persistence) | 0.708 | 316 | 437
LR, no feature engineering | 0.761 | 301 | 395
LR, with lags (J-1/J-2/J-3) | 0.778 | 288 | 381
LR, lags + seasonality | 0.792 | 279 | 368
Lasso (L1) | 0.788 | 282 | 372
Ridge (L2), FINAL MODEL | 0.789 | 282 | 371
Random Forest | 0.800 | 274 | 362
XGBoost | 0.801 | 272 | 360
Solar Production Forecasting · Machine Learning · Streamlit Dashboard
07

## Slide 8
05 · MODEL CHOICE
Why Ridge, not Random Forest or XGBoost?
5-fold cross-validation inside the training period (2020–2023): RF and XGBoost score the same test R² as Ridge (within 0.01), with a much wider train/test gap.
Model | R² train (CV) | R² test (CV) | Train-test gap
Ridge, chosen | 0.767 | 0.742 | 0.025
Random Forest | 0.855 | 0.740 | 0.115
XGBoost | 0.818 | 0.748 | 0.069
Ridge stays stable (train-test gap of about 0.02). RF and XGBoost score the same in test (within 0.01) with a 3 to 5x larger gap: we prioritize robustness.
A physical limit, corrected
Ridge, like any linear model, has no awareness that radiation can't be negative: it can predict slightly below 0 on low-radiation winter days. Predictions are therefore clipped to 0 (np.clip) before display and export, a correction that can only reduce error, never increase it.
Solar Production Forecasting · Machine Learning · Streamlit Dashboard
08

## Slide 9
06 · RESULTS
Forecast vs reality: final model (Ridge)
2025 predicted vs. actual radiation, a representative year from the 2021-2026 out-of-fold evaluation (22,150 predictions).
Solar Production Forecasting · Machine Learning · Streamlit Dashboard
09

## Slide 10
06 · RESULTS
Forecast vs reality: residual analysis
Residuals over the full 2021-2026 test period (predicted minus actual, national daily mean): errors stay centered near zero. They are larger in spring and summer in absolute terms, but summer is the best-predicted season in relative terms (21% vs 32% in winter).
Solar Production Forecasting · Machine Learning · Streamlit Dashboard
10

## Slide 11
07 · GOVERNANCE
Governance, compliance & monitoring
Public, aggregated data, open licences, and how the model would be followed in production.
1
GDPR
No personal data: weather, production and capacity are public and aggregated by region, and the dashboard collects no user data.
Even at the 8 km grid scale, weather data stays non-personal. GDPR would only apply with individual households’ meter data, outside the project’s scope.
2
Data licences
Etalab Open Licence (Météo-France, SDES), RTE eCO2mix terms of use and ODbL (OpenStreetMap): all sources credited in the README.
Copies of the raw files kept, since Météo-France changed its file layout after our download.
3
Technology choices
Python stack (pandas, scikit-learn, Streamlit). Raw Météo-France files strained memory: chunked loading, and only 2020–2026 kept.
At larger scale (2010–2019, or the 8 km grid), Polars or DuckDB would be needed. Docker and Hugging Face give a free, reproducible deployment.
4
Production monitoring
Weekly MAE compared with the naive baseline, with an alert if the error drifts above a set threshold.
Quarterly retraining, data-drift checks, and versioned code and data (Git).
Solar Production Forecasting · Machine Learning · Streamlit Dashboard
11

## Slide 12
07 · LIMITATIONS & NEXT STEPS
What's left to improve
The current model's known limitations, and the paths considered to go further.
LIMITATIONS
NEXT STEPS
A single horizon (J+1)
No J+2/J+7 forecast for longer-term planning.
Observed weather, not forecasts
The model uses measured weather for today; a real J+1 forecast would need Météo-France forecast data.
Radiation as a proxy
Production is a theoretical 20% conversion per m², not RTE's actual output.
Extended forecasts, J+2/J+3/J+7
For longer-term energy planning.
Use weather forecasts as inputs
Move from a retrospective model to an operational forecast.
Predict actual production
Once precise installed-capacity data is available (SDES publishes it quarterly only), or using recent production levels to track the fleet’s growth.
Solar Production Forecasting · Machine Learning · Streamlit Dashboard
12

## Slide 13
SUMMARY
From raw data to a production forecasting dashboard
26,676 observations, 12 regions, 6 years of Meteo-France x RTE x SDES data
Time-respecting validation (TimeSeriesSplit + GridSearchCV). Ridge chosen for its stability: −15% error vs "tomorrow = today" (R² ≈ 0.79 on 2024–2026 data)
Business impact: ~70 MWh/year of forecast error avoided for a 10,000 m² plant
Thank you for your attention.
Any questions?
Solar Production Forecasting · Machine Learning · Streamlit Dashboard
13
Streamlit dashboard in production: interactive EDA and next-day production estimates derived from the radiation forecast